Implementing the Continuous Fourier Transform by 
the Discrete Fourier Transform

丁老師編寫

For a input function x(t), we want to calculate its Fourier transform (FT)
                            	(1)
Then, we want to implement the FT digitally. First, we sample the t-axis and the f-axis as  
                         t = n(t,     f = m(f.  	(2)
Then, (1) is converted into  
                  , 	(3)
                    ,      	(4)
            where ,    .          	(5)
The range of n ( (((, () and m ( (((, () are impractical in implementation. Suppose that the value of x1[n] is known only when n1 ( n ( n2:       
                    ,    n1 ( n ( n2,              	(6)
We also choose (f to satisfy     
               ,   N is some integer, N ( N0 = n2 ( n1 +1,  	(7)
       i.e.,       where Fs = 1/(t is the sampling frequency. 	(8)
Then, (5) becomes  
                 .     	(9)
Since             
               where k is an integer,	(10)
(9) can be rewritten as
             .        	(11)
where ((n))N means the modulus operation (即 n 除以 N 的餘數)。      
If we set 
            for n1 ( n ( n2,               	(12)
         if there is no n in the range of n1 ( n ( n2 that satisfies h = ((n))N, 
then (11) becomes      
                .              	(13)
Therefore, we can use the N-point DFT to calculate the FT of x(t).

I then summarize the process for calculating the FT of x(t) by the N-point DFT as follows

(Step 1): Choose N to satisfy   
          N ( N0,   N is an integer,  N0 is the number of input samples, see (7).    	(14)

(Step 2): Form the N-length sequence x0[n]      
         for n1 ( n ( n2,               	(15)
      if there is no n in the range of n1 ( n ( n2 that satisfies h = ((n))N,

(Step 3): Perform the N-point DFT for x0[n]    
                     .  	(16)

(Step 4): Multiply the result by (t        
                              	(17)

(Step 5): Shift the right-half part of X1[m] to the left.

X2[m] = X1[m]     for 0 ( m < N1,      where N1 = round(N/2),        	(18)
          X2[m(N] = X1[m]   for N1 ( m < N.

(Step 6): ,  	(19)
        where  ,    m = N1(N, N1(N+1, ..., 0, 1, ..., N1(1.   	(20)

Note:

(a) Do not forget Steps 4 and 5

(b) The method can only calculate the spectrum in the range of 
              f ( ((fs/2, fs/2) where fs = 1/(t.           	(21)
To calculate the spectrum at higher frequency, we should choose smaller (t.

Example:

Perform the Fourier transform for the following signal:

x((t) = 3,  x(2(t) = 3,  x(3(t) = 6,  x(4(t) = 6,  x(5(t) = 3,  x(6(t) =6,  x(7(t) = 6,  x(8(t) = 2,   
x(n(t) is unknown when n ( [1, 8]   	(22)

(Step 1) Choose an N such that N is no less than the input samples

The input has 8 points. Therefore, we can choose N = 12 > 8.

(Step 2) Form a 12-length sequence x0[h]  
   x0[h] = x(h(t)   for h = 1, 2, 3, …, 8,                  	(23)
   x0[h] = 0       for h = 0, 9, 10, 11.

(Step 3) Perform the 12-point DFT for x0[n]  
                         	(24)

(Step 4) Multiply X0[m] by (t = 0.05:

(Step 5) Shift the right-half part of X1[m] (m = 6, 7, …, 11) to the left.

(Step 6): ,  	(25)
   where  ,     m = (6, (5, ...., 4, 5.

Matlab code

N=12;                    	% Step 1

x0=[0 3 3 6 6 3 6 6 2 0 0 0];   	% Step 2

X1=fft(x0)*0.05;                   	% Steps 3 and 4

X2=X1([round(N/2)+1:N, 1:round(N/2)]);  	% Steps 5

f=[-6:5]/12/0.05;                     	% Steps 6

plot(f, real(X2), '-o', f, imag(X2), 'r-o'); axis([-11,10,-1,2])

# Text boxes

速記法

做 N 點的 DFT

(a) N 注意一件事：N 要不少於輸入點數

(b) Input 注意一件事：

用 modulus 和 添零，形成N-length input

(c) Output注意二件事：

(i) 要乘上 (t, (ii) 並且將 DC 置於中央

(d) 將 m 變回 f， f = m (f，注意一件事：

(f  = sampling frequency 除以 N

x0[h]

X0[m]

X1[m]

blue:  real part,   red:  imaginary part

blue:  real part,   red:  imaginary part

X2[m]

blue: real part, 
red: imaginary part

X(f)

blue: real part, 
red: imaginary part

f (Hz)

|X(f)|

f (Hz)