## Slide 1: MPEG-4 Part 2 (MPEG-Visual)

## Slide 2: MPEG-Visual
Tools
  Subset of coding functions that support specific features
Objects
  Video elements
Profiles
  Subset of coding tools
Levels
  Define constraints on buffer memory

## Slide 3: The Simple Profile
VOP (Video Object Plane)
I-VOP (Intra)
P-VOP (Inter)

## Slide 4: I-VOP
DCT: 8x8
Quantization
Zig-zag scan
Last-Run-Level
Entropy Coding

## Slide 5: Quantization
Only define inverse quantization
Method2 (H.263 Quantization) for simple profile
Method1 (MPEG-4 Quantization) for advanced simple profile

## Slide 6: Quantization-Method 2
QP (step size) is in [1,31]
DC = DC_quantized × dc_scaler
For all short header (simple profile), Intra DC dc_scaler = 8
  Else, refer to Table 5.4
For others transformed coefficients including AC and Inter DC,

## Slide 7: P-VOP
Motion Compensation: 16x16 macroblock
Half pixel resolution
Each macroblock could either be coded in Inter-mode or Intra-mode
Inter-mode macroblock contains motion vector (differentially encoded) and coded residual coefficients of every 8x8 block

## Slide 8: Coding Efficiency Tools
Four motion vectors in one macroblock
Unrestricted motion vectors
Intra prediction of DC and first row/column of AC (optional)

## Slide 9: Transmission Efficiency Tools
Resynchronization marker
Data partitioning
  e.g. coding mode, DC coefficient (intra), motion vector (inter) in first partition while AC and DC coefficient (inter) in second partition
Reversible VLCs

## Slide 10: The Advanced Simple Profile
B-VOP
  Forward prediction: from previous I/P VOPs
  Backward prediction: from future I/P VOPs
  Average of forward/backward prediction: from previous/future I/P VOPs
Quarter-pixel motion compensation

## Slide 11: Quantization-Method 1
for intra and for inter

## Slide 12: Global Motion Compensation (GMC)
Sends up to 4 GMVs for each VOP
MV is calculated by interpolation
Coded as S-VOP (S is for “sprite”, which will be mentioned later)

## Slide 13: Interlace
Horizontal movements reduce correlation
Field/Frame DCT mode
16*8 motion compensation

## Slide 14: The Advanced Real Time Simple Profile
NEWPRED tool
  Requires extra memory to store previous VOPs

## Slide 15: The Advanced Real Time Simple Profile Cont’d
Dynamic Resolution Conversion (DRC)
  Limited bitrate channel
  Half sampled both horizontally and vertically before encoding

## Slide 16: Coding of Arbitrary Shaped Region (Core profile)
Binary shape coding
Motion compensation coding
Texture coding

## Slide 17: Binary Shaped Coding
Alpha blocks
  Binary or grey scale
  3 cases: transparent (outside), opaque (inside), boundary
  Encoded by context-based arithmetic encoding

## Slide 18: Binary Shaped Coding Cont’d
Intra: as context
  Set undefined pixels value as nearest neighbor inside the current BAB
Inter: as context
  to in current VOP and to in reference VOP

## Slide 19: Motion Compensated Coding
Padding
  Pad mean if both side have value
  Padding order: boundary > transparent

## Slide 20: Motion Compensated Coding Cont’d
Transparent MB should be padded as well
If only one neighbor boundary MB
  Horizontally or vertically extrapolation
If more than one neighbor boundary MB
  Left > Top > Right > Bottom
If no neighbor boundary MB
  Fill it with , where N is bits per pixel

## Slide 21: The Main Profile – Grey Shaped Coding
Grey scale alpha mask
  Binary support mask (coded by CAE)
  Grey scale alpha plane (coded by DCT)
Transparency information may not be identical

## Slide 22: The Main Profile – Static Sprite Coding
S-VOPs (Static Sprite VOPs)
Two ways to transmit
  Basic: sent entirely at the start
  Low latency: updated piece by piece
Both methods contain up to 4 warping parameters
Low latency contain “sprite pieces”
  Static-sprite-object
  Static-sprite-update

## Slide 23: The Advanced Coding Efficiency Profile – SADCT
Improve coding efficiency for boundary MBs

## Slide 24: The N-bit Profile
Limited display
Support color depth from 4-12 bits

## Slide 25: Scalable Video Coding
Spatial scalability
  Base layer & Enhancement layer
    Subsample input
    Encode the reduced-resolution frame to form the base layer
    Decode the base layer and up-sample to the original resolution
    Subtract the full-resolution frame from this prediction frame
    Encode the difference to form the enhancement layer
Temporal scalability

## Slide 26: Fine Granular Scalability (FGS)

## Slide 27: The Simple Studio Profile
Aim to encode video nearly-lossless
No temporal prediction (that is, only I-VOPs)