## Slide 1: Simple Eye Tracking by Depth Information And introduction to methods
葉明昌

## Slide 2: Flow
Camera Capture
Preprocessing
Convolution &
Thresholding
Postprocessing
Approximation
Large RGB (target)
Depth (assistance)
Main goal: Shrink the original image significantly by reasonable ways
Two gray-level image: Left eye and Right eye
and their neighborhoods
Two binary image: Left eye and Right eye candidates
Exclude the non-eye candidate region by color information (hsv)
Two binary image that both have exact one connected-component

## Slide 3: Captures

## Slide 4: RGB
Captured by camera
  I use Azure Kinect now, which might be replaced later
The task is to find eyes in this input
Issue 1: too large
  1920*1080 by the camera
  Many cv algorithms are O(MN)
  Cropping or simply resize?
Issue 2: Contain many non-face regions
  Increase the execution time to no purpose
  Even worse, it can cause error
  Simply resize cannot remove the regions
How to crop?

## Slide 5: Depth
Typical way to highlight the face area: face detection
  However, face detection usually need eye detection itself to implement
    Take the branch for the root
Another fast way: depth information
  People in camera should have “shallow” depth value
Depth image is take with Azure Kinect depth sensor
4

## Slide 6: Preprocessing
1920
1080
Some point
in original image
64
64
Some point
in left eye image
Denote
Lh( and Rh) is a series of transformation

## Slide 7: Preprocessing
Three thing to do
  1. Get two small enough image (64*64), L and R
  2. L should include left eye, R should include right eye
  3. Record the parameter that used for the preprocessing
Following is cascade of transformation to highlight L/R eye
  Let’s call them Lh{} and Rh{}, respectively

## Slide 8: Preprocessing
For depth image D:
  1. Thresholding by the 3rd percentile p3 , get binary image B = ( p3-k<= D <= p3+k )
  2. Find center of mass (Cx, Cy) for B
The binary image B might contain body part
  Then we can take like RGB(Cx:Cx+63, Max(y)+32:Max(y)+95) for left eye part

## Slide 9: Convolution
1. Special gray level – skin color projection
  We want to make the difference between skin and the eyes as large as possible
  Select a point S=(rs,gs,bs) in white part (skin) of B
    Upper, leftmost or rightmost (most likely to be face) may be a good choice
  Project all pixels P onto (rs,gs,bs)
  Use its length = as the gray level value

## Slide 10: Convolution
Integral image and Haar-like feature (ref: [1])
Make sure that the sum of filter elements is 0
Source: Figure.5 in [1]

## Slide 11: Convolution
2. Convolute the gray scale image with 2 3-block haar-like feature
  One is horizontal, use the property that human eyes structure is white-black-white
  One is vertical, use the property that skin is lighter than eyeball
  O(MN) + 2*O(1)*O(MN), M=N=64
If the constant is restricted to be 1 and -1
  Trick 1: introduced in last page, 12 addition for each element
  Trick 2: Add/Substract newest column/row, and Substract/Add oldest column/row
    2C( or 2R) addition for each element, R and C is the filter size
If not
  At most, we only need 3MN multiplication
Typical 2D convolution is O(MNlog(MN))
  Like some filter based on

## Slide 12: Thresholding
3. After convolution:
  (1). thresholding the vertical and horizontal result
  (2). AND the two binary image, then we get eye candidates
Issue: eye size may vary
  Use multiple filter in the same structure but different size
  Convolute the filter with images in different size
Issue: False Positive or False Negative
  For false negative, we can adaptively adjust the threshold for step.3
  For false positive case, we can use the following method as post-processing

## Slide 13: Postprocessing
Use color information
  Fast and doesn’t need further processing
  Property 1: Above and below the eye pixels are skin pixels
  Property 2: Next to the eye pixels are sclera pixels
HSV Color Space (cone image & formula source: Wikipedia:HSL and HSV)
  Can be formulated as a cone
  R at 0, G at , B at
  S = 1-min(R,G,B)/max(R,G,B)
  V = max(R,G,B)
  L
    Norm of (x,y,z) can be used as another gray level value

## Slide 14: Postprocessing

## Slide 15: Absolute Position
Center of Mass
  For left eye part:
Circle Fitting
After finding ), apply to it
  By this way, we can approximate the position of eyes in original picture
Overall Performance
  Execution time: 0.9s for 11 frames → Try more cases (ongoing)
  Platform: MATLAB R2019b → Transplant to C# code can increase speed
  CPU: Intel(R) Core(TM) i5-8300H CPU @ 2.30GHz

## Slide 16: Circle Fitting(Ref: [2])
Image source: [2]

## Slide 17: Relative Position(sight)
Need information of white part of eye to determine the relative position of eyeball
  Can use HSV to find white part in the 64*64 image
  Unlikely to have interference
Now, we have 4 binary image: LeftWhite, LeftBlack, RightWhite and RightBlack
  OR the white and black image, get the whole eye image E
  Use XOR(E, dilate(E)) to get boundary of eye
  Separate E to get upper boundary UB and lower boundary LB
  Use quadratic approximation to get the parabola that fit UB and LB
By ‘a’, we can determine looking upward/downward
Calculate the intersection of UB and LB
  Use this information to determine looking leftward/rightward

## Slide 18: Relative Position(sight)

## Slide 19: Relative Position(sight)
Grading policy
  If eye look at “center”
    Any answer that is different from “center” gets 0, otherwise gets 1
  If eye look at 3, 6, 9, 12 o’clock direction
    1: correct “right”, “down”, “left”, “up”
    0.5: one correct term, but a redundant direction (e.g. up left)
  If eye look at 1.5, 4.5, 7.5, 10.5 direction
    1: correct combination of “up, down” and “left, right”
    0.5: miss a direction in x or y dimension
Result: 14/18

## Slide 20: References
[1] Paul Viola and Michael J. Jones, “Robust Real-Time Face Detection”, International Journal of Computer Vision 57(2), 2004, pp. 137-154
[2] I.KASA, “A Circle Fitting Procedure and Its Error Analysis”, ieee transactions on instrumentation and measurement, March 1976, pp. 8-14